## Slide 1: ROCO218: Control Engineering Dr Ian Howard Lecture 2 Modelling electrical circuits with differential equations

## Slide 2
Where
i is the current in A
v is voltage in V
R is the resistance in Ω
Resists the flow of current
Electrical resistance

## Slide 3
Where
i is the current in A
v is voltage in V
L is the inductance in H
Electrical inductance

## Slide 4
Where
i is the current in A
v is voltage in V
C is the capacitance in F
Therefore
Also
Where Q is charge
Electrical capacitance

## Slide 5
One capacitor and one resistor in series
The source and resistor may be equivalent to a circuit with many resistors and sources
vr(t)
R
C
vs(t)
+
–
vc(t)
+
–
+
–
A First-order RC Circuit

## Slide 6
This is a first order linear differential equation
Adding up voltages
Ohms law
Current proportional to
rate of change of charge
Substitute I from
capacitor expression
Rearranged
Voltages in an RC circuit

## Slide 7
Adding up voltages
Ohms law
Voltage proportional to
rate of change of current
Substituted values
This is also a first order linear differential equation
Rearranged
Current in an LR circuit

## Slide 8
Any circuit with a single capacitor, a single inductor, an arbitrary number of sources, and an arbitrary number of resistors is a circuit of order 2
The source and resistor may be equivalent to a circuit with many resistors and sources
Any voltage or current in such a circuit is the solution to a 2nd order differential equation
vs(t)
R
C
i (t)
L
+
–
2nd order LCR circuits

## Slide 9
Adding up the contributions to overall applied voltage
Series RLC circuit

## Slide 10
Adding up the contributions to overall applied current
Parallel RLC circuit

## Slide 11
Element | V/I Relation | Comments
Resistor |  | V = I R R has SI unit Ohms
Capacitor |  | Q = CV C has SI unit is Farads
Inductor |  | L has SI unit Henrys
Summary: RLC Characteristics

## Slide 12: ROCO218: Control Engineering Dr Ian Howard Lecture 2 Modelling mechanical systems using differential equations

## Slide 13
where
f is force in N
k is the spring constant in N/m
Resists with opposing force proportional to extension of movement
Compression & extension springs

## Slide 14
where
T is torque in Nm
k is the spring constant in Nm/rad
Torsional springs

## Slide 15
Where
f is force in N
C is viscosity in Ns/m
Dampers/ shock absorber
Resists with opposing force proportional to velocity of movement
Like moving your hand in water – resistance proportional to how fast you move
Dampers and dashpots

## Slide 16
Where
f is force in N
m is mass in Kg
a is linear acceleration in m/s2
Resists with opposing force proportional to acceleration of movement
Inertial Mass

## Slide 17
Where
T is torque in Nm
J is moment of inertial in Kgm2
Resists with opposing torque proportional to angular acceleration
Moment of Inertia

## Slide 18
Adding up the contributions to overall force
Spring mass damper system

## Slide 19: ROCO218: Control Engineering Dr Ian Howard Lecture 2 Circular movement

## Slide 20
Constant speed circular movement
The distance travelled by the mass in time T seconds is given by
Consider a point mass travelling around central point in a circle at a constant speed with rotational period
Therefore in T seconds is rotates though an angle of 2π radians
Thus angular velocity ω is given by
The average speed at which is does so it therefore
Substituting in
Note also
The rotational frequency can be related to rotational period T

## Slide 21
Simple derivation of centrifugal acceleration
Consider the moving mass
As the mass rotates through an angle of θ the tangential velocity of the mass changes from v1 to v2
Mass moves a distance Δd
Velocity magnitude stays constant but its direction changes so velocity changes by Δv
By consideration of similar triangles with the same angle θ
if Δd is very very small is can be approximated by
Substituting in this value
As Δt tends to 0, term Δv/Δt represents acceleration
Since from before

## Slide 22
Chain rule for single variable differentiation
Consider the one variable equation corresponding to a function of a function
Writing
Chain rule gives
For example if
In this case let

## Slide 23
Calculus derivation of centrifugal acceleration
We can write down the projections of the mass position along the x and y axes
We can write mass position vector P(t) as sum of its base vector components
Differentiating both sides wrt time t gives

## Slide 24
Calculus derivation of centrifugal acceleration
Now angular velocity is given by
Which is a constant if speed is constant. Substituting into
Differentiating the expression again

## Slide 25
Calculus derivation of centrifugal acceleration
Now acceleration A(t) is given by
Taking the modulus of both sides
Note that
Is just the radius of the circle
Or as from before

## Slide 26: ROCO218: Control Engineering Dr Ian Howard Lecture 2 Modelling a DC motor

## Slide 27
N
S
Fleming's Left Hand (Motor) Rule
Thumb = Direction of Conductor Motion
Fore Finger = Direction of Magnetic
Middle Finger = Conventional Current Direction
Left Hand
The Left Hand Rule to determines the movement direction of conductor carrying current

## Slide 28
forces:
force on current leading conductor in a magnetic field
torque:
sum of all forces at the distance to the rotating axis
influencing parameters:
geometry
field density
winding number
Depend on the design
current direction towards brush
force
force
current direction towards flange
magnetic
field
Motor Torque constant Kt
Motor torque Tm is given by
Notes: This schematic motor cross section shows the origin of the simple proportional relationship between torque and current. The underlying physical principle is the force on a current conducting wire in an external magnetic field.
The amount of torque produced depends on the geometrical arrangement of the winding, its distance to the rotation axis, the density of winding turns, the strength of the magnetic field in the air gap and the amount of current applied. With the exception of the current all the other parameters are defined by the intrinsic design and cannot be changed on the finished motor. That's why they are summed up in one constant, the torque constant kM. The amount of torque produced by the motor becomes proportional to the motor current.

## Slide 29
Multiple coils reduces torque ripple
Overall torque summed from both coils
Typical small armature
with multiple multi-turn coils

## Slide 30
R = Armature resistance (in ohms)
L = Armature inductance (in Henrys)
J = Moment of inertia for the motor rotor (kg.m2)
b = Motor viscous friction constant (in N.m.s)
Kt = Motor torque constant (in N.m/A)
Ke = Electromotive force constant (in V/rad/sec)
DC motor dynamics
V applied voltage, I is the current drawn
R resistance of coil and brush contact
L is the coil inductance
EMF is back emf of motor
Lets relate output speed of motor to the applied voltage!

## Slide 31
Motor torque Tm is given by the current multiplied by the torque constant of the motor
Mechanical resisting torque Tr is given by inertia and viscous friction
Therefore equating the two terms gives torque equation
DC motor dynamics
Rearranging torque equation

## Slide 32
Summing voltages around the circuit gives voltage equation
DC motor dynamics

## Slide 33
State space DC motor dynamics
Now writing
from
Now writing
from

## Slide 34
State space DC motor dynamics
So we have the two equations
We can write these two equations in matrix form
If we want to observe the speed of the motor as the output y

## Slide 35
State space DC motor dynamics
As we will later see the two equations describe the motor in state space form
By observation of standard state space form
We see that

## Slide 36: ROCO218: Control Engineering Dr Ian Howard Lecture 2 Numerical solutions of 1st order differential equation

## Slide 37
Ordinary differential equation (ODE)
contains one or more functions of one independent variable and its derivatives
For example
Differential equations
Partial differential equation
may compare more than one independent variable
contains unknown multivariable functions and their partial derivatives.
For example

## Slide 38
Local linear approximation of gradient
xo
yo
y
x
Δx
Δy
x1
y1
Consider a function y=f(x)
When x=x0 then y=y0
As we increase the value of x by Δx
we reach a point where x1=xo+Δx
Similarly this increases y by Δy
reaching the value y1=yo+Δy
Thus
The gradient of the curve at (xo, yo) is the tangent to the curve at this point

## Slide 39
Local linear approximation of gradient
xo
yo
y
x
Δx
Δy
x1
y1
In general the differential of a function is given by
So the gradient at (xo, yo) can be approximated by
Which is only strictly true in the limit where dx tends to zero
In our case

## Slide 40
Local linear approximation of gradient
xo
yo
y
x
Δx
Δy
x1
y1
We can use the relationship to iteratively estimate y1 from yo since
Writing Δx as step size h
We can use this to give next estimate of y1 if we know xo and the gradient at (xo yo )

## Slide 41
Euler’s method of integration
This is Euler’s method to solve a 1st order differential equation!
It uses a local linear approximation to the gradient
We can iteratively estimate the value of the function at the next step
Given the relationship
Where
t is time
y is the output value of the function
At initial time to the output is yo
At future time t(n+1) the output is y(n+1)
h is the step size
Notice the simulation error will rise as the step size increases!

## Slide 42
This is a first order linear differential equation
Adding up voltages
Ohms law
Current proportional to
rate of change of charge
Substitute I from
capacitor expression
Rearranged
Remember: Voltages in an RC circuit

## Slide 43
Simulation of voltages in an RC circuit
Here we wish to compute the evolution of Vc with time. We know that
From the iterative relationship we derived previously
One of your lab assignments is to implement this simulation in Matlab!
Matlab also has more sophisticated numerical methods to solve differential equations- e.g. ode45

## Slide 44
Implementing Euler integration in Matlab
We can write simple script using the update equation to estimate capacitor voltage is given by the equation

## Slide 45
Implementing Euler integration in Matlab

## Slide 46
Using ode45 to perform integration
help ode45
Solve non-stiff differential equations, medium order method.
[TOUT,YOUT] = ode45(ODEFUN,TSPAN,Y0)
with TSPAN = [T0 TFINAL] integrates the system of differential equations y' = f(t,y) from time T0 to TFINAL with initial conditions Y0.
ODEFUN is a function handle.
For a scalar T and a vector Y, ODEFUN(T,Y) must return a column vector corresponding to f(t,y).
Each row in the solution array YOUT corresponds to a time returned in the column vector TOUT.
To obtain solutions at specific times T0,T1,...,TFINAL (all increasing or all decreasing), use TSPAN = [T0 T1 ... TFINAL].

## Slide 47
Using ode45 to perform integration

## Slide 48: Interlude 10 minute break

## Slide 49: ROCO218: Control Engineering Lecture 2 Introduction to Simulink

## Slide 50
Used to model, analyze and simulate dynamic systems using block diagrams.
  Provides a graphical user interface for constructing block diagram of a system – therefore is easy to use.
Can be used for simulation of various systems:
  Linear, nonlinear
Input signals can be arbitrarily generated:
  Standard: sinusoidal, polynomial, square, impulse
  Customized: from a function, look-up table
Output signals can be stored or demonstrated in different ways.
  However modeling a system is not necessarily easy !
Simulink

## Slide 51
First launch Matlab
Then in the Matlab command window launch slimulink
Do this at the >> prompt by typing simulink
and press  Enter
Launching Simulink

## Slide 52
Simulink window

## Slide 53
Next click the new-model icon in the upper left corner to start a new Simulink file
Create a new model

## Slide 54
This opens a window
Your workspace

## Slide 55
Drag selected components into workspace
Add components

## Slide 56
Connect components
Click run button
Click on scope
to open display
Connect components and run model

## Slide 57
Main components exhibit dynamics:
  integrators,
  transfer function
  zero-pole description
Parameters can be set for various components
Also math components:
  gain (amplifier) kx : x a scalar
  addition (a+b+c)
  product (abc)
  number of i/o points and the sign of each are adjustable
Available components blocks

## Slide 58
Sources: input signals
  constant, step, ramp
  pulse, sine wave, square wave
  from data file
  signal generator
  a clock to record time
Sinks: for output display or storage
  export to workspace; you can give a name
  to the variable, such as u, y, x, etc.
  scope
  digital display
Many components blocks available

## Slide 59
Save your model

## Slide 60: ROCO218: Control Engineering Dr Ian Howard Lecture 1 Simulink 2nd order differential equation

## Slide 61
Build a Simulink model that solves the following differential equation
  2nd-order mass-spring-damper system
  zero initial conditions
  input f(t) is a step with magnitude 3
  parameters: m = 0.25, c = 0.5, k = 1
Mass-spring-damper system

## Slide 62
  The simulation diagram for solving the ODE is created step by step.
  After each step, elements are added to the Simulink model.
Create the simulation diagram

## Slide 63
summing block
First, solve for the term with highest-order derivative
Make the left-hand side of this equation the output of a summing block
Create the simulation diagram

## Slide 64
Drag a Sum block from the Math library
Double-click to change the block parameters to rectangular and + - -
Create the simulation diagram

## Slide 65
Add a gain (multiplier) block to eliminate the coefficient and produce the highest-derivative alone
summing block
Create the simulation diagram

## Slide 66
Drag a Gain block from the Math library
Double-click to change the block parameters.
Add a title.
The gain is 4 since 1/m=4.
Create the simulation diagram

## Slide 67
summing block
Add integrators to obtain the desired output variable
Create the simulation diagram

## Slide 68
Drag Integrator blocks from the Continuous library
Add a scope from the Sinks library.
Connect output ports to input ports
Label the signals by double-clicking on the leader line
ICs on the integrators are zero.
Create the simulation diagram

## Slide 69
summing block
c
k
Connect to the integrated signals with gain blocks to create the terms on the right-hand side of the equation of motion
Create the simulation diagram

## Slide 70
Drag new Gain blocks from the Math library
Double-click on gain blocks to set parameters
Connect from the gain block input backwards up to the branch point.
Re-title the gain blocks.
To flip the gain block, select it and choose Flip Block in the Format pull-down menu.
c=0.5
k=1.0
Create the simulation diagram

## Slide 71
c
k
f(t)
input
+
-
-
x(t)
output
Bring all the signals and inputs to the summing block
Check signs on the summer
Complete the model

## Slide 72
Double-click on Step block to set parameters. For a step input of magnitude 3, set Final value to 3
Drive with a step function

## Slide 73
Final Simulink model

## Slide 74
Run the simulation