## Slide 1: ROCO218: Control Engineering Dr Ian Howard Lecture 4 Transfer Functions

## Slide 2
A differential equation is an equation which contains derivative terms
Differential equation can often be used to describe a dynamical system in the time domain
For example, a differential equation can capture the relationship between the force input f(t) and output position x(t) of a mass-spring damper
differential
equation
f(t)
y(t)
transfer
function
F(s)
Y(s)
Transfer functions
A transfer function is an expression that describes a system the s-domain that relates the output to the input
To get to the s-domain we use the Laplace transform

## Slide 3
Given the s-domain input X(s) and output Y(s) the transfer function H(s) is given by the ratio of the output Y(s) to the input X(s)
H(s) = Y(s) / X(s)
H(s)
X(s)
Y(s)
Transfer functions
Consider a system in the s-domain with input X(s) and output Y(s)
The output of the system can Y(s) therefore be found by multiplying the input X(s) with the transfer function H(s)
Y(s) = X(s)H(s)
For example, if the input signal is a step then
X(s) = 1/s
Therefore in this case
Y(s) = H(s)/s

## Slide 4
H1(s)
X(s)
H2(s)
Y(s)
Transfer functions in series
We can use block diagrams to pictorially expresses flows and relationships between elements in system represented by their transfer functions
Such signal flow graphs can often be simplify using simple rules
Consider two blocks in series
Z(s)
Looking at midpoint we see that
Z(s) = X(s)H1(s)
Y(s) = Z(s)H2(s)
Y(s) = X(s)H1(s)H2(s)
Therefore
X(s)
H1(s)H2(s)
Y(s)
So we can represent H1(s) and H2(s) in series by a single block with a transfer function equal to their product H1(s)H2(2)
This result generalized to multiple blocks in series

## Slide 5
H1(s)
X(s)
H2(s)
Y(s)
Transfer functions in parallel
Consider two blocks in parallel
The output from the summer is
Y(s) = X(s)H1(s)+ X(s)H2(s
Y(s) = X(s)(H1(s)+H2(s))
Therefore
X(s)
H1(s)+H2(s)
Y(s)
So we can represent H1(s) and H2(s) in series by a single block with a transfer function equal to their sum H1(s) + H2(2)
+
This result generalized to multiple blocks in parallel and also to subtraction rather than addition

## Slide 6
This is a very important result
for feedback control!
Closed loop system
G(s)
X(s)
H(s)
Y(s)
+
Feedback path
Forward path
Input
Output
E(s)
-
+
Substituting in error term E(s)
Collecting factors of Y(s) terms
E(s)G(s)
Y(s)H(s)
Calculating the transfer function

## Slide 7
control
Gc(s)
plant
Gp(s)
feedback
H(s)
pre-filter
G1(s)
post-filter
G2(s)
reference input, R(s)
error, E(s)
plant inputs, U(s)
output, Y(s)
feedback, H(s)Y(s)
Typical block diagram for simple feedback controller
YPf(s)
X(s)
Let us compute the overall transfer function of this system
To do so we first simplify the structure
-
+

## Slide 8
control
Gc(s)
plant
Gp(s)
feedback
H(s)
pre-filter
G1(s)
post-filter
G2(s)
Typical block diagram for simple feedback controller
YPf(s)
X(s)
Let us compute the overall transfer function of this system
To do so we first simplify the structure
Lets consider the control and the plant
Can be combined into a single block
-
+

## Slide 9
Control and plant
Gc(s)Gp(s)
feedback
H(s)
pre-filter
G1(s)
post-filter
G2(s)
Typical block diagram for simple feedback controller
YPf(s)
X(s)
Let us compute the overall transfer function of this system
To do so we first simplify the structure
Lets consider the control and the plant
Can be combined into a single block
-
+

## Slide 10
Control and plant
Gc(s)Gp(s)
feedback
H(s)
pre-filter
G1(s)
post-filter
G2(s)
Typical block diagram for simple feedback controller
YPf(s)
X(s)
Now consider the feedback loop
Can be combined into a single block
-
+

## Slide 11
Typical block diagram for simple feedback controller
Now consider the feedback loop
Can be combined into a single block
Gc(s)Gp(s)
_______________
[1+Gc(s)Gp(s)H(s) ]
pre-filter
G1(s)
post-filter
G2(s)
YPf(s)
X(s)

## Slide 12
Gc(s)Gp(s)
_______________
[1+Gc(s)Gp(s)H(s) ]
pre-filter
G1(s)
post-filter
G2(s)
Typical block diagram for simple feedback controller
YPf(s)
X(s)
Now consider the three blocks in series
These can be combined into a single block

## Slide 13
G1(s)Gc(s)Gp(s)G2(s)
_______________
[1+Gc(s)Gp(s)H(s) ]
Typical block diagram for simple feedback controller
YPf(s)
X(s)
Now consider the three blocks in series
These can be combined into a single block

## Slide 14
2. Moving a summing point from behind a block
Combining blocks in cascade or in parallel
Block diagram reduction summary

## Slide 15
5. Moving a pickoff point from ahead of a block
3. Moving a summing point ahead of a block
4. Moving a pickoff point from behind a block
Block diagram reduction summary

## Slide 16
6. Eliminating a feedback loop
7. Swap order of two neighboring summing points
Block diagram reduction summary

## Slide 17: ROCO218: Control Engineering Dr Ian Howard Lecture 4 Transfer function RLC example

## Slide 18
Adding up the contributions to overall applied voltage
Series RLC circuit

## Slide 19
From differential equation of voltage
Taking Laplace transforms
Series RLC circuit in the s-domain
Similarly for capacitor voltage

## Slide 20
Transfer function is given by
Series RLC circuit in the s-domain
Cancelling current term

## Slide 21
Consider the mass-spring-damper system shown below:
Describe using differential equation of motion
Balancing the forces gives:
Analysis of a simple mechanical system
Use these parameters
M = 0.5 kg
b = 5 N s/m
k = 10 N/m
F = 1 N

## Slide 22
The Laplace transform gives
Remember in the general case the Laplace transform of differentials include initial conditions
Analysis of a simple mechanical system
So given

## Slide 23
Setting initial conditions to zero
Use these parameters
M = 0.5 kg
b = 5 N s/m
k = 10 N/m
F = 1 N
So given
Analysis of a simple mechanical system

## Slide 24: ROCO218: Control Engineering Dr Ian Howard Lecture 4 Modelling a DC motor with transfer function

## Slide 25
Motor torque Tm is given by the current multiplied by the torque constant of the motor
Mechanical resisting torque Tr is given by inertia and viscous friction
Therefore equating the two terms gives torque equation
Revision: DC motor dynamics

## Slide 26
Summing voltages around the circuit gives voltage equation
Revision: DC motor dynamics

## Slide 27
Taking Laplace transforms of the differential equations that describe the motor mechanical dynamics:
Becomes
Motor solution using Laplace transformations

## Slide 28
Taking Laplace transforms of the differential equations that describe the motor voltages:
Becomes
Motor solution using Laplace transformations

## Slide 29
Substituting
Into
Motor solution using Laplace transformations
and thereby laminating current I(s)

## Slide 30
setting Kt = Ke= K gives
Motor solution using Laplace transformations
So from
factoring out 1/K

## Slide 31
Result of a transfer response output position for a DC electric motor given its input voltage
Can differentiate this expression to get the transfer function for speed by multiplying by the transfer function of a differentiator (=s)
Motor transfer function

## Slide 32
Expand the expressing into powers of s so can be directly used with Matlab tf function.
Becomes
Simulink model simulation transfer function

## Slide 33
R = 8.152 Ω
L = 3.252 mH
J = 0.04248 kg.m2
b = 0
Kt = 53.965 N.m/A
Ke = 53.965 V/rad/sec
Use real motor parameter values:
Use Matlab to calculate Simulink parameters

## Slide 34
Excite circuit with a step function
Use multiplexers to joint step and output signals
Display outputs using scopes
Building the Simulink model simulation

## Slide 35
Use real motor parameter values in transfer function
Enter transfer function parameters
Better to use Matlab to compute values in workspace and refer to them here is Simulink
Makes it easy to change values without having to update numerical values

## Slide 36
The speed plot when zoomed in will look like this.
Angular velocity settles time is about 4ms
Examine angular speed plot

## Slide 37
Shows linear increase in angular position when step function activated
Examine angular position plot

## Slide 38
It is easy to generate a Bode plot of transfer functions.
We can use the Matlab bode function
This plots the amplitude and phase response of the transfer function
Bode plots of the transfer function

## Slide 39
Bode plots of the transfer function

## Slide 40
Underdamped response.
Overshoot of 0.5.
Final value of 3.
Is this expected?
Output results

## Slide 41: Interlude 10 minute break

## Slide 42: ROCO218: Control Engineering Dr Ian Howard Lecture 4 Poles and zeros

## Slide 43
The poles of a transfer function are the values of s that make the function evaluate to infinity.
The value of s can be visualized on the s-plane
The poles are therefore the roots of the denominator polynomial
For example: the expression
Poles of a transfer function
  Has a pole at s = -1
  And a pole at s = -3
Complex poles always appear in complex-conjugate pairs
The transient response of system is determined by the location of poles

## Slide 44
The zeros of a transfer function are the values of s that make the transfer function evaluate to zero.
They are therefore the zeros of the numerator polynomial
For example: The expression
Zeros of a transfer function
has a zero at s = -2
Complex zeros always appear in complex-conjugate pairs

## Slide 45
Plotting poles on the complex plane
x
x
x
x
x
x
Real number
component axis
Complex number component axis

## Slide 46
Effect of a -ve real pole
System exhibits exponential decay
The signal will eventually decay to a constant value of zero
Therefore the system is stable
Exponential decay
x

## Slide 47
Effect of a -ve real part complex pole
System exhibits exponential damped sinusoidal decay
The signal will eventually decay to a constant value of zero
Therefore the system is stable
Damped sinusoid
x
x

## Slide 48
Effect of a +ve real part complex pole
System exhibits exponentially sinusoidal growth
The signal will eventually go to infinity (in a mathematical model)
Therefore the system is unstable
Exponentially growing sinusoid (unstable)
x
x

## Slide 49
A system is stable if bounded inputs produce bounded outputs
The complex s-plane is divided into two regions:
Stable region, which is on the left half of the plane
Unstable region, which is on the right half of the s-plane
Stable behavior
s-plane
stable
unstable
x
x
x
j

x
x
x

## Slide 50
If the output of a process grows without bound for a bounded input, the process is referred to a unstable
If the real portion of any pole of a transfer function is positive, the process corresponding to the transfer function is unstable
If any pole is located in the right half plane, the process is unstable.
Unstable behavior
s-plane
stable
unstable
x
x
x
j

x
x
x

## Slide 51
Stable feedback system
Consider the open loop transfer function
We see the gain margin is 15.6dB
This corresponds to a linear gain of 6.0256
Unity feedback losed loop transfer function is given by
When K=1 this has the corresponding Bode plot

## Slide 52
Stable feedback system
Thus we can change the location of the close loop poles by changing the gain K
If we plot the locations of the poles and zeros on the s-plane as gain K changes, we get what is known as the ”root locus” plot
From the plot we can see when they poles moves to the unstable RHS of of s-plane
Factor K thus affects pole location

## Slide 53
Stable feedback system
Below we use a low gain of 3 and the system is stable

## Slide 54
Unstable feedback system
However as the gain goes above the gain margin of the system will go unstable
Below we use a higher gain of 7 and the system is stable

## Slide 55: ROCO218: Control Engineering Dr Ian Howard Lecture 9 PID control

## Slide 56
Plant characteristics are often fixed
We need to design a controller to achieve required plant performance
Have to be careful because feedback system can go unstable!
So what should the controller be?
Simple feedback controller

## Slide 57
Place a PID controller C(s) in series with the plant P(s) and make use of negative feedback
A well-designed control system will ensure
  We reach a target value quickly
  Without overshoot
  With low steady state error.
Adding a PID controller

## Slide 58
PID parallel pathways
PID is a mathematical algorithm that the controller uses to compensate for load fluctuations and changes in set point.
These operations are executed on the error between the set point and the actual value.
They determine how the plant will react to change
A PID controller consists of 3 parallel elements that are located in the forward path in a feedback controller scheme located before the plant
The plant to be controller received the sum of these three processed signals as its input
The 3 PID elements have different effects

## Slide 59
The proportional term directly relates to the error value at the present moment in time
The proportional gain is given as Kp
Proportional gain can improve rise time
If Kp too high the system can become unstable
Proportional term

## Slide 60
The integral term relates to a past values of the error up to the present point in time
It is proportional to both the magnitude of the past error and its duration
The integrator gain is given as Ki
Integral term eliminates residual steady-state error
Integral term

## Slide 61
The derivative term that is proportional to the slope of the error over time and relates to a prediction of what the error will be like in the future
The differentiator gain is given as Kd
Derivative term improves settling time and stability of the system
Derivative term

## Slide 62
Relationship between input error e(t) and output control signal u(t) is thus captured by the differential equation:
PID differential equation
u(t)
e(t)

## Slide 63
Tuning PID parameters strongly affects controller performance
Changing PID controller characteristics

## Slide 64
Differential equation that described PID controller
Taking Laplace transformations and rearranging gives the transfer function for the PID controller:
Transfer function of PID controller

## Slide 65: ROCO218: Control Engineering Dr Ian Howard Lecture 9 Simple PID control example

## Slide 66
Consider the mass-spring-damper system shown below:
Describe using differential equation of motion
Balancing the forces gives:
Analyze a simple mechanical system

## Slide 67
Given the differential equation of motion
The Laplace transform gives
Use these parameters
M = 0.5 kg
b = 5 N s/m
k = 10 N/m
F = 1 N
Analyze a simple mechanical system

## Slide 68
Lets use Matlab to generate a Bode plot of the transfer function of the mechanical system
You should get a plot that looks like this:
Find the -3dB point
  Where response goes down -3dB from max
Estimate rise time
  Time needed for value to go from 10% to 90%
Bode plot of a transfer function

## Slide 69
Lets use the Matlab step function to plot the step response of the system.
Look at the Matlab help for the function step
Pass it a time vector that gives time values between 0 and 2 seconds in steps of 0.01 seconds.
What is the rise time here?
Generate step response

## Slide 70
Lets now place a PID controller C(s) in series with the plant P(s) and make use of negative feedback
A well-designed control system will ensure
  We reach a target value quickly
  Without overshoot
  With low steady state error.
Adding a PID controller

## Slide 71
Relationship between input error e(t) and output control signal u(t) captured by the differential equation:
PID differential equation

## Slide 72
Controller gives
Plant gives
Product of these series elements gives
Example: Overall open-loop transfer function

## Slide 73
Given this feedback arrangement and
serial controller and plant configuration
The close loop transfer function is
Overall closed-loop transfer function

## Slide 74
So given
The close loop transfer function is
Example: Overall closed-loop transfer function

## Slide 75: ROCO218: Control Engineering Dr Ian Howard Lecture 9 Simulating PID in Matlab

## Slide 76
Matlab can perform symbolic manipulation
  (similar to Mathematica)
The tf function generates Matlab format transfer functions
You can use it to specify a complex transfer function
Or even a simple simple ones
Then use mathematical manipulation on the variable to generate other transfer function relationships
You can of course always do the maths by hand if you like
But Matlab is less likely to make a mistake than a human!
You can then use Matlab functions like Bode and Nyquist to directly analyze the transfer functions
Building plant transfer function in Matlab

## Slide 77
Define plant parameter variables
Build the plant transfer function
Displaying content of P gives
Building plant transfer function in Matlab

## Slide 78
Define example PID parameter variables
Build the PID controller transfer function
Displaying content of PIDC gives
Building plant transfer function in Matlab

## Slide 79
Given plant and PID transfer functions
Open-loop transfer function is their product
Displaying content of OL gives
Calculating open-loop transfer function

## Slide 80
Given plant and PID transfer functions
Closed-loop transfer function is given by
Displaying content of FB gives
Open-loop transfer function is their product
Calculating closed-loop transfer function

## Slide 81
Kp = 1
Not much has changed
from open loop response!
Feedback control with only proportional gain

## Slide 82
Kp = 300
Quite different from open loop response!
Reaches unity
Faster rise time
But oscillations
Feedback control with only proportional gain

## Slide 83
Kp = 300
Use Matlab step function to show response characteristics

## Slide 84
Kp = 300
Feedback control with only proportional gain
Peak response

## Slide 85
Kp = 300
Feedback control with only proportional gain
Rise time

## Slide 86
Kp = 300
Feedback control with only proportional gain
Settle time

## Slide 87
Fast rise time
No oscillations
Overshoot
But quite good!
Exact response of course depends on values
With proportional & differential gain
Kp = 300 and Kd = 50

## Slide 88
Low steady-state error
With full PID gains
Kp = 300, Kd = 50, Ki = 300

## Slide 89
Just P
PD
PID
Open loop
But precise response depends on appropriate tuning of all feedback components
Compare