## Slide 1: ROCO218: Control Engineering Dr Ian Howard Lecture 8 Transfer function of a SFC system

## Slide 2
Transfer functions of SFC system
Given the state space equations
We showed previously that the transfer function of this state space model is given by the expression
So assuming D is zero we have

## Slide 3
Transfer functions of SFC system
The SFC gain K effectively changes the A matrix
Therefore we can modify the transfer function G(s) accordingly
So the transfer function for the state space system
Becomes
As we know, by applying full state feedback leads to the relations

## Slide 4
The reference input R(t) will be processed by the SFC system
Effect of transfer function on reference input
To achieve good tracking of the reference input we require that
as
Driving the system with a unit step input, we require the output to be unity
To achieve this we need to scale the reference input by a gain

## Slide 5
Effect of transfer function on reference input
Using the final value theorem, we require that time output driven by step lends to unity
So to achieve this we will scale the input so that
Substituting in the transfer function for the SFC system
We need to scale the reference input by this value to ensure unity DC gain of the SFC system
This leads to an expression for the scaling

## Slide 6: ROCO218: Control Engineering Dr Ian Howard Lecture 8 Integral action

## Slide 7
Scaling the input reference a good practice to ensure output reaches the input target
However with pure SFC we do not make use the system output Y(t)!
If we don’t use the output, the system will need to be calibrated to operate well
Therefore requiring we have an exact process model is undesirable!
State space feedback control

## Slide 8
Integral action
Remember one of the primary uses of feedback is to allow good performance in the presence of uncertainty!
So we can use integral feedback to make use of the output
Here the controller uses an integrator to achieve zero steady state error
To achieve integral feedback we create a state within the controller that computes the integral of the error signal
This is is then used as a feedback term as denoted by the green path on the schematic above

## Slide 9
To achieve integral feedback we augment the system by adding another state Z
The state Z is the integral of the error between the desired output R(t) and actual output Y(t)
Thus the standard state space equation
augmented with the state Z becomes
Using feedback control if the augmented state we see that
Integral action

## Slide 10
Given the equation
Let the constant terms be represented by the coefficients
Choosing state space representations
Remember: velocity control inverted pendulum

## Slide 11
From the state space representation of the velocity controlled inverted pendulum
Where output y is the pendulum angle θ
Remember: Velocity control inverted pendulum

## Slide 12
Remember: Augmented velocity control inverted pendulum
In practice we can to control cart position as well as angle and angular velocity!
Otherwise it might never stop moving!
To do so we can add a third state x3 to represent cart position
Since the control signal is cart velocity, the differential of x3 is simply given by the input velocity control signal
Therefore we can write

## Slide 13
Adding integral action to the VCIP
We now want to use the cart position to generate error integrated over time
To do so we can add a fourth state x4 to represent integrated cart position error
To achieve this we further augment the system matrices
Notice we update the integral state by selecting the position state x3 to generate the (y-r) term used for integral action
Here we assume the reference value is zero
We didn’t change y to implement this

## Slide 14
Substituting in the coefficients leads to the equations
Adding integral action to the VCIP
Finally we can design the feedback gain vector K needed to implement full feedback state control using the Matlab place command

## Slide 15: ROCO218: Control Engineering Integral control exam solutions

## Slide 16
Q4: SFC, integral control and observer

## Slide 17
For system
Full state feedback requires that
So system equations become
Q4: SFC, integral control and observer

## Slide 18
From state space system
Q4: SFC, integral control and observer

## Slide 19
We require that the eigenvalues λ of the controller system are at -3,-2
This means we will want the following characteristic equation for the eigenvalues
The eigenvalues λ of the closed loop system are given by
Substituting in values for B we have
Q4: SFC, integral control and observer

## Slide 20
So e expanding
We now need to match the coefficients in the desired eigenvalues characteristic equation using the appropriate gain vector K
Q4: SFC, integral control and observer
This gives the characteristic equation for the system
We want the characteristic equation

## Slide 21
Integral action can be implemented by introducing another state z in the system such that
For a pure state feedback system
Adding in the additional state for integral action this leads to he expression
We also amend the feedback control to include weighted contributions from the state z
Q4: SFC, integral control and observer

## Slide 22
An observer can be used to estimate system state using efference copy of the motor command
To make the process, robust the output from the system can also be used to correct the state estimate
For the plant of the system
For state estimator
Where matrix 2x2 L represent a scaling of the error between actual and predicted output
To ensure the estimator is stable and initial conditions decay away, it is necessary to choose L such that the expression
Has eigenvalues with negative real parts
The feedback control is given by
Q4: SFC, integral control and observer

## Slide 23: ROCO218: Control Engineering Dr Ian Howard Lecture 8 Optimal control

## Slide 24
Remember: State feedback control
We showed previously state feedback control provides a means to move the eigenvalues of a system from their open loop values
In an open loop state space system
Stability determined by location of poles which are the eigenvalue of matrix A
Gives rise to the closed loop system
Stability determined by location of poles which are the eigenvalue of matrix (A-BK)
Substituting in state feedback as input

## Slide 25
Remember: State feedback control
The corresponding signal flow graph is shown below
When a system is fully controllable its eigenvectors poles can be placed arbitrarily by choosing the value of K
But how to place poles is often not obvious!
Therefore a more principled methods to choose K is often useful

## Slide 26
Optimal control
Instead of direct pole placement, optimal control makes use of a performance criterion
To do so we define a ‘cost function’ which lets us minimize some quantity of the control process
For example imaging we a driving a car:
We could minimize the time required to go from A to B
We could minimize the fuel used to go from A to B
We could minimize the financial cost to go from A to B
= Final Time
= Fuel Used
= £ Cost of trip

## Slide 27
Optimal control
Often a quadratic performance measure is adopted
To make analysis easier
leads to well behaved solutions
Is the weighted square distance of state from its origin
Affects convergence rate: rise time and settling time
Large Q means get good tracking as expense of large input
Is the weighted square of control input activity
Penalizes large and aggressive inputs
Large R means little input needed at expense of good tracking
We need to optimize the performance index for the given state space system
The term
The term
Where typically

## Slide 28
Optimal control
We want to find the corresponding gain K that minimizes J
From the expression for cost
The solution by dynamic programming
This leads to the expression for the optimal gain
where R is invertible and P is symmetric and satisfies the algebraic Riccati equation

## Slide 29
Example: Force optimal control of mass position
Consider control of a 1Kg mass.
Since f = ma
Defining the two state variables
Writing in state space notation we have
Therefore

## Slide 30
We want to find optimal control that minimizes
This can be formulated as an LQR problem with
To solve the minimization problem, we first solve the algebraic Riccati equation:
Since we have a 2x2 A matrix, we solve for the matrix P which is symmetric Matrix with the following entries:
and
Example: Force optimal control of mass position

## Slide 31
Substituting in the system matrices algebraic Riccati equation becomes
Evaluating terms
Example: Force optimal control of mass position

## Slide 32
Evaluating terms
Example: Force optimal control of mass position

## Slide 33
So therefore
Thus the elements of the matrix must be zero
Example: Force optimal control of mass position

## Slide 34
Solving the equations
will have P positive definite (P > 0), if and only if p1 > 0 and det(P) > 0
Example: Force optimal control of mass position

## Slide 35
the expression for the optimal gain
Example: Force optimal control of mass position

## Slide 36
Optimal control gain design using Matlab
In Matlab the optimal gain can be found using the lqr command
The Matlab document page is as follows: