## Slide 1: ROCO218: Control Engineering Dr Ian Howard Lecture 8 Real inverted pendulum practical

## Slide 2
Inverted pendulum main components
By moving the cart to the left and the right it is possible to balance the pole and keep it upright

## Slide 3
Pendulum system with the rod shown vertically in its unstable position
Stand allows the pendulum to rotate freely and avoid collisions.
Pendulum system mounted on its aluminum profile stand

## Slide 4
Inverted pendulum main components

## Slide 5
Pendulum drive motor and carriage mechanism
The drive pulley attached to the the stepper motor can be seen on the right and the attachment clamp for the pendulum rod can be seen on the left.

## Slide 6
Inverted pendulum microcontroller and stepper driver
Arduino Mega
A4988 Stepper Motor Controller
Cooling fan on lid
USB
connection

## Slide 7
Arduino Mega connections
Digital I/O
Analog inputs
Power outputs
USB input
Encoder attached to DI interrupt pins: encoderPinA = 18, encoderPinB = 19
Hall sensors attached to DI interrupt pins: HallSensorLeft = 20, HallSensorRight = 21
Stepper controller attached DO to pins: dirPin = 4, stepPin = 5, enPin = 6

## Slide 8
Microcontroller ATmega2560
Operating Voltage 5V
Input Voltage (recommended) 7-12V
Power via the USB connection
Digital I/O Pins 54
Digital I/O Pins which provide PWM output 15
Digital I/O Pins which provide interrupts 6
Analog Input Pins 16
DC Current per I/O Pin 40 mA
DC Current for 3.3V Pin 50 mA
Operate at 5 volts
Pins have internal pull-up resistor (disconnected by default) of 20-50 kOhms
Flash Memory (of which 0.5 KB used by bootloader) 256KB
SRAM 8 KB
EEPROM 4 KB
Clock Speed 16 MHz
Arduino Mega summary
Reason we need Mega and cannot use Uno

## Slide 9
Open the Arduino main window shown on the left
Download is available at www.arduino.cc
Use a USB A to B cable to plug you computer into the Arduino
Setup the port connection
Setup the board type
How to start coding: Software setup
Editor input area

## Slide 10
Arduino’s programming language is a version of C
Most C commands work in the sketch editor
Four basic components of Arduino program
  Initialization
  Setup
  Loop
  User defined functions
Arduino Mega is designed to allow it to be reset by software running on a connected computer
Programming the Arduino

## Slide 11
Include any extra libraries you are using
All variables need to be initialized
A=4; will not work int a= 4; will
Define variables you will assign later
  Int a,b,c;
Remember data structures
  Int, double, float, char, string ….
Programming the Arduino: Initialization

## Slide 12
Initialization for the Arduino board
Usually begin serial communication
Usually assign digital pins to input or output
For example:
Programming the Arduino: setup
Void means setup will not output anything
pinMode defines the state of digital pins to OUPUT or INPUT.
Serial.begin(9600) opens serial communication at 9600 baud

## Slide 13
Loop is the main portion of the Arduino code
Loop is what the microcontroller will do forever
This is very much like a never ending for loop
Programming the Arduino: loop

## Slide 14
Compile
Upload
Serial Monitor
Under tools make sure Board is the board you and using and Serial port is checked and is the correct port
Compiling and uploading code

## Slide 15: ROCO218: Control Engineering Dr Ian Howard Lecture 8 Simple Arduino example programs implementing functionality needed to control the inverted pendulum

## Slide 16
Menu control test program flow chart
Look at example Arduino program:
ProcessControlTest.ino

## Slide 17
Menu control test program
Define functions that are called to generate desired control
Define function to print out menu options on request
Setup the serial output
Process commands
Arduino setup function
Arduino loop function

## Slide 18
Menu control test program
If there is an incoming command
Read command and display it
Use a switch function to decode the command and call the appropriate command function

## Slide 19
Menu control test program

## Slide 20
Hall effect magnetic sensor circuit
Simple switch activated by the application of a magnetic field
When south pole of magnet brought up to this sensor, LED is switched on

## Slide 21
Shutdown control using Hall sensor flow chart
Look at example Arduino program:
SimpleHallSensorTest.ino

## Slide 22
Shutdown control using Hall sensor limit switches
SunFounder Analog Hall Switch Sensor Module
0v to GND
+5v power to VCC
Digital output on D0
Hall sensors activated by neodymium magnet on carriage
Neodymium magnet on carriage
Sensors need to stop control when pendulum carriage reaches its
end of travel to the left and to the right

## Slide 23
Shutdown control using Hall sensor limit switches
Define digital inputs
Use pins that support interrupts
Define control stop function
Define flag
Left sensor callback function
Right sensor callback function

## Slide 24
Shutdown control using Hall sensor limit switches
Use serial interface
Only perform processing if flag active
Enable processing
Associate Hall callbacks with pins
Arduino setup function
Arduino loop function
Setup Hall sensors
Processing goes here

## Slide 25
Generates a relative position signal suitable for positioning tasks
Rotation direction recognition
Speed information from number of pulses per time unit
Standard solution for many applications
Single output types only used to determining the speed
Digital incremental encoder

## Slide 26
Read encoder flow chart
Look at example Arduino program:
SimpleEncoderTest.ino

## Slide 27
Arduino incremental encoder test program
Include the encoder class
Define digital input pins that support interrupts to connect to encoder
Build the encoder object as global variable

## Slide 28
Arduino incremental encoder test program
Use serial interface
100ms delay so doesn’t run too fast
Print out angle in radians
Arduino setup function
Read encode
Print out raw encoder count
Choose output format
Arduino loop function

## Slide 29
Arduino incremental encoder test program
Plot output using serial monitor

## Slide 30
Use micro step mode
This implements a gradual transition between pole positions
This leads to smoother operation that full-step
Microstep stepper motor control
Microstepping

## Slide 31: A4988 Stepper Motor Controller
Intelligent current control up to 2A
Set stepping mode via control pins – set to 4x micro stepping
Simple step and direction control interface
To operate: Need to generate
  control pulses (1 pulse per micro step)
  direction signals (so motor turns in desired direction)
https://www.pololu.com/product/1182
Stepper shield

## Slide 32
CStepper velocity control class flow chart

## Slide 33
CStepper velocity control class flow chart
Define pins used for stepper
Define signals variables
Setup digital output pins
Record this pointer
needed for callback

## Slide 34
CStepper velocity control class flow chart
Define this pointer
Define interrupt service routine that will generate pulses
Setup a timer
Attach interrupt routine that will be called by timer

## Slide 35
CStepper velocity control class flow chart
Pulse generation function
Toggle pulse state
Inc or dec pulse count depending on direction
Write pulse state to digital output

## Slide 36
CStepper velocity control class flow chart
Enable the stepper
Disable the stepper
Set stepper direction
set timer period
Stepper Function

## Slide 37
Arduino stepper velocity control flow chart

## Slide 38
Arduino stepper velocity control test program
Include the stepper class
Define the movement parameters
Define the encoder pins
Define stepper motor parameters
Build the velocity control stepper motor object

## Slide 39
Arduino stepper velocity control test program
Setup serial I/O
Setup timer
Turn off the steppers to start with
Regularly poll the stepper control
Put in 10ms delay
Regularly poll the command manager
Arduino setup function
Arduino loop function

## Slide 40
Arduino stepper velocity control test program
Poll function for command manager
Read and echo back incoming command
Decode the commands
Switch off stepper option
Switch on stepper option
Report help option

## Slide 41
Arduino stepper velocity control test program
Poll function for stepper speed generation
Calculate current sine wave modulated output velocity
Determine motor direction
Determine stepper pulse period needed
Use the pulse period and direction

## Slide 42
Arduino stepper velocity control test program
Look at example Arduino program:
StepperVelocityTest.ino

## Slide 43
CSFC3 class control flow chart

## Slide 44
SFC with observer C++ implementation

## Slide 45
SFC with observer C++ implementation

## Slide 46
SFC inverted pendulum control flow chart

## Slide 47
Arduino inverted pendulum state space control
Arduino loop function
Read encoder
If system active proceed
If balancing not started
look for start
Else if balancing started
Scale encoder input and get time
Compute SFC controller output
Compute pulse period and motor direction
Set desired motor speed and direction
Regularly service command menu